## Slide 1: Improved Arneson Control System(ACS) for P444 series Super Dvora Mk III
By LT (IT) DSA AS Gunashinghe

## Slide 2: Introduction:
The ACS is an innovative craft/ship digital steering and trim control system based on the well-known Arneson Surface Drive (ASD) system. The system uses state of the art hardware and software technology to implement PID (Proportional Integral Differential) control algorithm to drive and control the craft propellers.

## Slide 3: Project Aim:
Improve low cost and more reliable system to control the craft propulsion system.

## Slide 4: Why need this system:
By looking at previous defects and number of occurrence ,PC is not suitable for such environment because of pitching and rolling, it will effect to PC hard disk directly though the mount on shock absorber. Also PC is general purpose machine and runs other process rather than ACS application.

## Slide 5: Why need this system cont..:
Supper Dovra MK III , has encountered with one of defect in steering system which non synchronizing of propeller movement with the wheel moment (Error message popped up as “System encountered an uncorrectable hardware error”) . due to instability of current system
The above error occurs periodically in P444 series craft. Ship builder attend to above error during the warranty period. But after warranty they won’t attend this issue free

## Slide 6: Advantages:
Improve system reliability.
Reduce maintenance cost .
By looking at previous defects and number of occurrence ,PC is not suitable for such environment because of pitching and rolling, it will effect to PC hard disk directly though the mount on shock absorber. Also PC is general purpose machine and runs other process rather than ACS application

## Slide 7: Present system

## Slide 8: Main parts of the ACS system :
The main parts of the ACS system are:
  Two control panels (which are also uses as displays)
  An industrial PC
  An Adaptors box
  An SCC (Solenoids Control Card) box
  Steering wheels
  Three dual proportional solenoids
  Four Electronic In Cylinder Transducer (EICT)

## Slide 9: Block Diagram:
CONTROL STATION (OPEN)
CONTROL STATION (CLOSE)
WHEEL(OPEN)
WHEEL
(CLOSE)
WHEEL_OPEN
WHEEL_CLOSED
SCC BOX
ADAPTORS BOX
PC
220 VAC
USB_CAN
USB_NMEA
GPS
DC POWER INPUT
10-36 VDC
SENSORS
ICT
SOLENOIDS
6
4
6
DVI
CLOSED
DVI_OPEN
CAN-2_SOLENOID + NFU + POWER
CAN-1_SOLENOID + NFU + POWER
CAN-1_OPEN + NFU + POWER
CAN-2_OPEN + NFU + POWER
CAN-1_CLOSED + NFU + POWER
CAN-2_CLOSED + NFU + POWER

## Slide 10: System Interface:

## Slide 11: Advantage of System Modification :
Increase the system reliability.
Reduce maintenance cost ( After warranty period ).

## Slide 12: System modification :
This project for replace conventional pc to single board computer .
SBC

## Slide 13: System modification Diagram:
SBC

## Slide 14: Steps to be completed in ACS System:
Analysis CAN(Control Area Network) Signal.
Develop application to control CAN device via single board computer.
Design user interface and test the system.

## Slide 15: Item Requirement & estimated cost

## Slide 16: Time Schedule
Milestone | Time In Months |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Study CAN Signal in current system |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Process control signal |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design circuit and developing CAN controller |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design UI and testing system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |